comments
- Much much more context and background
- Diagrams of systems and how investigated in general
- FERROMAGNETIC RESONANCE – also sweeping the field strength
- Illustrate why useful – distinguish from nmr
- Field space diagrams

---
Exploring the Dynamical Behaviour of Spin Waves Through Energy Absorption Interferometry
Felix Biggs

---
Overview
- Introduction, Methodology
- Dipole properties & responses
- EAI
- Further investigation of properties

---
Introduction
- General technique, based on partially coherent energy absorption
- Used previously on electric dipoles – here will be applied to magnetic
- Spin waves – large static field aligns and smaller time varying excites

---
EAI
- The excitation is caused by phase-locked sources
- P(Δϕ) measured → fringe → complex visibility
- Source positions varied, EAI then reconstructs modes of system
- Requires only P! So widely applicable.

---
Methodology
I. Discretise system (always possible using DDA)
  - Calculate response matrix of given system
  - Simulate its response to given sources
II. Use EAI to reconstruct response
III. Investigate system properties further

---
Implementation
- Use MATLAB – highly efficient for matrix manipulation and plotting
- Make code modular so changing system is only modifying a few parameters
- Investigate `known' properties to check for bugs

---
Theory of Magnetic Dipoles
- Evolve according to Landau-Lifshitz-Gilbert:
- For single dipole in strong fixed field, response dyad (similar to tensor):
\frac{d{\bf {m_{j}}}}{dt}=-\gamma_{j}\mu_{0}{\bf {m_{j}}}\times{\bf {H}}_{j}^{tot}+\frac{\alpha_{j}}{|{\bf {m_{j}}}|}({\bf {m_{j}}}\times\frac{{d{\bf {m_{j}}}}}{dt})
\overline{\overline{\chi}}(\boldsymbol{r})=\sum_{j}\frac{\gamma_{j}\mu_{0}m_{j}^{s}\omega}{(\omega_{0j}^{2}-\omega^{2})-i\omega\Gamma_{j}}\overline{\overline{S}}_{j}\delta(\boldsymbol{r-\boldsymbol{r_{0j}}})
\overline{\overline{S}}_{j}=\frac{\omega_{0j}}{\omega}\boldsymbol{\hat{i}\hat{i}}-i\boldsymbol{\hat{j}\hat{i}}+i\boldsymbol{\hat{i}\hat{j}}+\frac{\omega_{0j}}{\omega}\boldsymbol{\hat{j}\hat{j}}

---
Discrete Version
- Use greens function from sources:
- This gives us complex amplitudes at dipoles:
- Then apply coupling and scattering to get h(tot)
\overline{\overline{\boldsymbol{G}}}(\boldsymbol{r},\boldsymbol{r'})=\frac{1}{|\boldsymbol{r}-\boldsymbol{r'}|^{3}}[3\overline{\overline{\boldsymbol{R}}}(\boldsymbol{r},\boldsymbol{r'})-\overline{\overline{\boldsymbol{I}}}]
h^{ext}\in\mathbb{C}^{2J}

---
Power Absorbed
- At a dipole, field is sum of ext, coupling and scattered (which destroys information):
- Define response matrix:
- Can be broken down into terms from scattering and coupling (kappa is scattering):
{\bf {H}_{j}}^{tot}={\bf {H}_{j}}^{dip}+{\bf {H}_{j}}^{ext}
<P>=\textrm{Tr}\left[H^{e}L\right]
H^{e} = <h^{e}h^{e*}>
{\textstyle m}=\chi{\textstyle h^{e}}+\chi{\textstyle G^{x}m}=(\chi^{-1}-{\textstyle G^{x}})^{-1}{\textstyle h^{e}}=\xi{\textstyle h^{e}}
L=\frac{\omega}{2}\mu_{0}\kappa^{\dag}\xi^{R}\kappa

---
Power Absorption: 1 Dipole, 1 Source
Circularly Polarised source at (1,1). Dipole at (0,0) with w0 = 1, gamma (damping) = 1/16. All constants set to 1 for simplicity.

---
Power Absorption: 2 Dipoles
Same source, same dipole properties but now two, at (0.4,0) and (-0.4,0), directly coupled with coefficient 0.3.

---
Power Absorption: 5 Dipoles
Same source, same dipole properties. Now 5, at (0.4,0) etc around (0,0), directly coupled with coefficient 0.3. 3 modes, lowest frequency one most easily excited.

---
Fringe from 2 sources, 10 dipoles
Green line shows sum of powers of two sources independently

---
How does this compare with theory?
- Lorentzian shape for 1
- 2 dipoles coupling – 2 modes expected - think about geometry for absorption
- 5 dipoles – lowest mode most excited
- Fringe – as expected
P(\nu)=\frac{\omega}{2}\mu_{0}\varint_{\nu}{\bf H}^{tot1*}({\bf r})\cdot\overline{\overline{\boldsymbol{\chi}}}(\boldsymbol{r})\cdot{\bf H}^{tot1}({\bf r})d^{3}{\bf r}=\sum_{j}\frac{\gamma_{j}\mu_{0}^{2}m_{j}^{s}}{2}[\frac{\omega\Gamma_{j}}{\omega^{2}(\frac{\omega_{0j}^{2}}{\omega^{2}}-1)^{2}+\Gamma_{j}^{2}}]\times{\bf H}_{j}^{tot*}\cdot\overline{\overline{{\bf S}_{j}}}\cdot{\bf H}_{j}^{tot}

---
Side note: Positive Power
- Looking at equations we see there are solutions giving negative power absorption (opposite direction rotation).
- i.e. S has -ve and +ve eigenvalues for w>w_0
- However we are manifestly in the steady state regime.

---
Side note: Positive Power 2
- These excitations would be 'damped out' in practice, so we remove them.
- This is done simply be decomposing the field at each dipole:
  h = a(1,i) + b(1,-i)
- Then set h = a(1,i)

---
Theory of EAI in Brief
- For two coherent sources:
- Assemble matrix H = [h1,h2,...hn] for n source positions
- Rewrite:
P=\mathrm{[h_{1}^{ext\dagger}}e^{-i\phi_{1}}+\mathrm{h_{2}^{ext}}e^{-i\phi_{2}}]\,\mathrm{L}\,\mathrm{[h_{1}^{ext}}e^{i\phi_{1}}+\mathrm{h_{2}^{ext\dagger}}e^{i\phi_{2}}]
\mathrm{L}=\sum_{nm}a_{nm}\mathrm{\tilde{h_{n}^{ext}}}\mathrm{\tilde{h_{m}^{ext\dagger}}}=\mathrm{\tilde{H}A\tilde{H}^{\dagger}}

---
EAI 2
- However a little maths shows us that:
- Where P(ii) is power absorbed by single source i, and P(ij) is power absorbed by both i and j, and phi is the phase difference.
- This neatly allows us to populate A, and if we know the source properties, calculate L using the H.
- It seems odd that we use our knowledge of source positions but makes sense if we use DDA.
P_{nm}=a_{nn}+a_{mm}+a_{nm}e^{i\phi}+a_{mn}e^{-i\phi}

---
EAI 3: SVD
- In general dim(A) != dim(H) so H is not invertible to find the dual.
- In this case we use SVD:
- We can also plot the complex visibility as a function of position(j) for fixed (i) to look at coherence lengths etc.
\mathrm{H}=\mathrm{U\Sigma V^{\dagger}}\implies\mathrm{\tilde{H}}=\mathrm{U\Sigma^{-1}V^{\dagger}};\;\mathrm{H^{\dagger}\tilde{H}=1}

---
Eigenvalues
- Once we have reconstructed L, we may diagonalise it.
- This gives the eigenvector excitations – i.e. the ways in which we can excite the sample in only one mode.
- Some examples are plotted for investigation of the systems – they illustrate that individual modes are simply Lorentzian

---
Eigenvalue responses: 2 dipoles
Same 2 dipole configuration as before. Responses due to each of 2 eigenvectors.

---
Eigenvalue responses: 5 dipoles
Two sets of degenerate modes, plus lowest freq one

---
Eigenvalue responses: 10 dipoles
Dipoles in line eigenvalues and excitation by source at (5,5). Most excited modes are 'fundamental', w1, sqrt(2)*w1 and 2*w1. Seems to be shown for other numbers. Interestingly they are also lowest modes available for end coupled version

---
Longer chains – some properties
- End coupling increases favouring of lowest mode excitation
- Tend to get multiples of sqrt(2) most excited
- Moving source closer excites higher modes more
- Quite obvious comparison with string modes

---
Discussion
- Individual eigenvector responses look as expected.
- Number of generally modes makes sense
- Can see slightly better if look at individual eigenvectors
- Interesting responses for linear chains to sources

---
Conclusions
- System gives expected responses
- EAI works for recovering those responses
- Responses are generally as expected
- Other things that I have looked at: coherence volumes, many different systems (especially circular ones), relative dipole orientations (with arrows) and magnetic field throughout space of various modes.

---
Questions?